Ping

1. Ping from the lab machine to the Raspberry Pi, 10 times, interval 0.2 seconds. Report the results.

10 packets transmitted, 10 received, 0% packet loss, time 1834ms
rtt min/avg/max/mdev = 0.044/0.051/0.083/0.010 ms

2. Ping from the Raspberry Pi to the lab machine, 10 times, interval 0.2 seconds. Report the results.

10 packets transmitted, 10 received, 0% packet loss, time 1808ms
rtt min/avg/max/mdev = 0.026/0.048/0.076/0.018 ms

3. Ping from the Raspberry Pi to the lab machine, 100 times, interval 0.001 seconds (use sudo).
Report the results, and discuss the differences between minimum, mean and maximum results.

100 packets transmitted, 100 received, 0% packet loss, time 99ms
rtt min/avg/max/mdev = 0.017/0.018/0.072/0.005 ms
Minimum and mean times are very close together with the max being much larger. This suggests there are a lot more near the minimum value rather than the maximum.

4.Ping from the Raspberry Pi to the lab machine, 10000 times using flooding (use sudo).
Report the results.

10000 packets transmitted, 10000 received, 0% packet loss, time 660ms
rtt min/avg/max/mdev = 0.016/0.017/0.470/0.010 ms, ipg/ewma 0.065/0.017 ms

5. Ping from the Raspberry Pi to the lab machine. Run measurements with 3 different intervals (0.01, 0.001, 0.0001) and at least 1000 measurements, and draw a cdf of your measurements results (one graph per interval).